## Slide 1: SPARK V
Basic I/O Interfacing and Programming

## Slide 2: AVR Programming Software
WINAVR:
  Open Source
  http://winavr.sourceforge.net/download.html
AVR Studio:
  Utilizes WINAVR in back end
  Debugger
  http://www.atmel.com/avrstudio/

## Slide 3: Input Output Ports
  ATMEGA 16 is 8-bit microcontroller with Advanced RISC Architecture.
  40 Pin Microcontroller
  There are 32 programmable I/O Lines
    Four 8 bit Port : A, B, C, D
  All I/O ports pins are bidirectional and can be configured individually.

## Slide 4: Input Output Ports
ATMEGA2560 have Ten 8 bit ports (A,B,C,D)
Each Port has three associated I/O registers:
1. Data Direction Register (DDRx) (x = A,B,C,D)
Sets individual pin of the port as input or output
2. Port Driver Register (PORTx) (x = A,B,C,D)
Sets individual pin of the port as 1 or 0 .
3. Port Pins Register (PINx) (x = A,B,C,D)
Reads data from the port if port is configured as input
DDR value | Status
1 | Output
0 | Input

## Slide 5: Configuring I/O Ports
Example 1: Make PORTD as output port with the following bit pattern
DDRD
PORTD
Step 1: Make Port D output port  DDRD = 0xFF
Step 2: Put data on the Port D  PORTD = 0xD5
D7 | D6 | D5 | D4 | D3 | D2 | D1 | D0 | HEX
1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | FF
D7 | D6 | D5 | D4 | D3 | D2 | D1 | D0 | HEX
1 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | D5

## Slide 6: Configuring I/O Ports
Example 2: Make PORTD input port with the following configuration
PORTD
Step 1: Make Port D output port  DDRD = 0x00
Step 2: Put data on the Port D  PORTD = 0xF0
D7 | D6 | D5 | D4 | D3 | D2 | D1 | D0 | HEX
1 | 1 | 1 | 1 | 0 | 0 | 0 | 0 | F0

## Slide 7: Configuring I/O Ports
Example 3 :
Make upper nibble of PORTD as output and lower nibble as input. Out 3 on upper nibble and read back data by PIND
Step 1: Make Port D’s Pin7 to Pin4 as output pins and
Pin3 to Pin0 as input pins DDRD = 0xF0
Step 2: Put data on Port D’s Pin7 to Pin4 and enable pullup for
Pin3 to Pin0  PORTD = 0x3F
Step 3: Read the data from Port D using PIN  temp = PIND
D7 | D6 | D5 | D4 | D3 | D2 | D1 | D0 | HEX
1 | 1 | 1 | 1 | 0 | 0 | 0 | 0 | Port Direction: DDRD F0
0 | 0 | 1 | 1 | 1 | 1 | 1 | 1 | Port Config:  3F

## Slide 8: First Program : Buzzer Interfacing
Vcc
Buzzer
PC3
To turn on the buzzer
Set PC3 pin Logic 1

## Slide 9: Buzzer Program
  Buzzer is connected to PORT C , pin 3
  Configure PORTC, 3rd pin as output.
  DDRC= 0x08; //0000 1000
  To turn ON the buzzer set PC3 output high
  PORTC = 0x08; //0000 1000
  To turn OFF the buzzer set PC3 output low
  PORTC = 0x00; //0000 0000

## Slide 10
Thank
You