## Slide 1: SPARK V
Motion Control using I/O Ports

## Slide 2: Various Motions of SPARK V
Forward
Reverse
Right Turn
Left Turn

## Slide 3: Various Motions of SPARK V
Soft Right
Soft Left

## Slide 4: Direction Control
  Two DC motors are connected to PB0, PB1, PB2, PB3 Pins of the microcontroller.
  Speed is controlled by Pin PD4 and PD5.
  IC L293D is used as a driver between the microcontroller and the DC motors.

## Slide 5: Direction Control
Microcontroller Pin | Function
PD4 | Pulse width modulation for the right motor (velocity control)
PD5 | Pulse width modulation for the left motor (velocity control)
PB0 | Left motor direction control
PB1 | Left motor direction control
PB2 | Right motor direction control
PB3 | Right motor direction control

## Slide 6: Block Diagram of L293D IC

## Slide 7: Logic table for direction control of Motors
Left Motor
Right Motor
Output on PORTA
Direction Of Robot
PB0
PB1
PB2
PB3
0
0
0
0
0x00
Stop
0
1
1
0
0x06
Forward
1
0
0
1
0x09
Backward
1
0
1
0
0x05
Hard Left
0
1
0
1
0x0A
Hard Right
0
0
1
0
0x02
Soft Left
0
1
0
0
0x04
Soft Right

## Slide 8: Motion Control Programming
Write function : INIT_PORTS();
Initialize Ports: Port A and Port L
  DDRB=0x0F; //0000 1111
  PORTB=0x00;
  DDRD=0x30; //0011 0000
  PORTD=0x30;

## Slide 9: Motion Control Programming
Call functions like:
  FORWARD();
  REVERSE();
  LEFT_TURN();
  RIGHT_TURN();
  STOP();
In between introduce delay:
  _delay_ms(1000);

## Slide 10
Thank
You